MATERIAL SAFETY DATA SHEET

DISTRIBUTOR:	Dixon Sealer & Supply, Inc.			Phone: 800-233-4966

R. 749 N. Keyser Ave.				Fax:     570-343-3053

Scranton, PA  18504-9722

PRODUCT NAME OR NUMBER:			        NPFA CLASSIFICATION

ULTRA BOND 2000				HAZARD RATING        DEGREE OF HAZARD

DUST PALLIATIVE – SOIL STABILIZER

0= LEAST

1= SLIGHT 	      HEALTH          1								 		  2= MODERATE            REACTIVITY   0										  3= HIGH		      FIRE                  0								 		  4 = EXTREME

#1) COMPONENT DATA

CHEMICAL COMPONENTS		%WT					C.A.S. NUMBER

Resin				60 To 65					C.A.S. # Resin 64742-11-6

Emulsifiers and Water			40 To 35

- 100

#2) PHYSICAL DATA

Boiling Point ((F)		  		212(

Vapor Pressure (mmHg  @  0(c) .1 		Percent

Vapor Density (AIR = 1):			1

Solubility in Water:				Readily Dispersible

Specific Gravity: (H²0=1):			1

Percent Volatile by Volume: 			25(C       up to 45% water

Evaporative Rate (Ethyl Ether = 1):		1

pH Information: 				5.0 - 7.0

Appearance and Odor: 			Light-brown color, no objectionable odor

#3) FIRE & EXPLOSION HAZARD DATA

Flash Point COC,  ((F): 			310(+

Extinguishing Media:  	Foam, water fog, dry chemical, CO2

Special Fire Fighting Procedures: 	 Do not enter confined fire space without proper protective equipment including self-contained breathing apparatus.

#4) REACTIVITY DATA

Stability:	Material is stable.  Avoid temperature above 180º and freezing.

Hazardous Decomposition Products:	Carbon monoxide, aldehydes and carbon dioxide from burning.  Oxides of nitrogen and sulfur may                          also be produced.

#5) HEALTH HAZARD DATA

Eyes:  This material is not expected to cause eye irritation.

Skin:  This material is not expected to cause skin irritation.

Ingestion:  Not expected to be acutely toxic by ingestion.  If swallowed, Do Not induce vomiting, call a physician.

Inhalation:  Fumes may be unpleasant and may produce nausea.  Remove the person to fresh air if respiratory discomfort occurs.

Effects of Overexposure:  Inhalation of high concentrations may cause dizziness, headache, or nausea.

Health Data: This material will be diluted further with water to use as a dust suppressant.   This product is expected to be practically non-irritating to the eyes.

Page 2

#6) EMERGENCY & FIRST-AID PROCEDURES

Inhalation:	If a large amount of mist is inhaled, move exposed person to fresh air and call a physician.

Contact to Skin:	If skin becomes wet, wash exposed area with soap and water.

Contact to Eye:	Immediately flush eyes with large amounts of water and continue flushing for 15 minutes.

#7) SPECIAL HANDLING INFORMATION

Respiratory Protection:	Use NIOSH approved respirator for particulates if overexposure to mist occurs.

Protection of Skin:	For prolonged or repeated exposures, use impervious clothing (boots, gloves, aprons, etc.).  Launder soiled clothes.  Properly dispose of contaminated leather articles including shoes, which cannot be decontaminated.

Protection for Eyes:	Wear safety goggles as splashes to the eyes may occur.

#8) ENVIRONMENTAL PRECAUTIONS

Spill:	Do not allow spill to enter sewers or water ways.  Remove all sources of ignition.  Absorb with appropriate inert material such a sand, clay, placed in drums or other suitable containers.

Method of Waste Disposal:	The disposal of this material must comply with federal, state and local regulations.

#9) ADDITIONAL INFORMATION

Handling and Storage:  	This product is not classified as hazardous under DOT regulations.  Store in closed containers.

Additional Information	This product is a water soluble emulsion and considered a Non-Placarded material for transportation.

MANUFACTURER DISCLAIMER:  While the information and recommendations contained herein are believed to be accurate, we make no warranty with respect hereto and disclaim all liability from reliance thereon.

Revision Date 01.02.2003